## Slide 1
SDR_RADIO
FM & AM Receive-Chain Architecture
Processing blocks, cross-thread data flow, and thread structure
FM RECEIVE CHAIN
Two threads now: acquire (mixer+
resample) / demod (FM+stereo+audio),
handed off via a bounded queue
AM RECEIVE CHAIN
New: TAMBroadcastReceiver — envelope
or synchronous (PLL) detection,
live-adjustable bandwidth
MODE SELECT
ModeCombo (FM/AM) in uSDRMain —
mutually exclusive, same TSDRRFSource
UPDATED — AM implemented, FM split across 2 threads

## Slide 2
WHAT CHANGED SINCE THE LAST REVISION
Two real fixes landed in the codebase
2
SDR_Radio — newVM Lazarus/FPC SDR receiver
uAMReceiver.pas (new)
• TAMBroadcastReceiver — same TComponent/Source shape as FM's receiver
• Envelope (diode-detector) or synchronous (Costas-loop PLL) demod, switchable live
• Bandwidth is a live-adjustable property (1–10 kHz) — rebuilds the chain, short click
• Single-threaded — AM's demod is a plain O(N) loop, no need for FM's split
uFMReceiver.pas (revised)
• Chain split into TFMAcquireThread + TFMDemodThread across a bounded queue
• Fixes audible distortion: on real ARM64 hardware the single-thread chain averaged over its per-epoch real-time budget, so drift compensation fired almost every epoch (a persistent buzz)
• Lets acquire (wideband) and demod (5 FIR filters + 2 resamplers) run concurrently on separate CPU cores instead of time-sharing one
Both receivers, side by side
FM (TFMBroadcastReceiver)
AM (TAMBroadcastReceiver)
Threads
2 — TFMAcquireThread + TFMDemodThread,
handed off via TBasebandQueue (drop-oldest)
1 — TAMDSPThread (plain tight loop)
Demod stage cost
Heavy: FM discriminator + stereo pilot
decode = 5 FIR filters + 2 resamplers
Light: envelope sqrt() or PLL rotate,
O(N), no filtering
Channel bandwidth
Fixed 200 kHz (broadcast-FM spec)
Variable 1–10 kHz, live-adjustable
Output
Stereo (L/R from pilot-locked decode)
Mono (duplicated to L=R)

## Slide 3
SYSTEM OVERVIEW
Component architecture — three sibling consumers, one Source
3
SDR_Radio — newVM Lazarus/FPC SDR receiver
SDR hardware
HackRF / RTL-SDR / SDRplay
TSDRRFSource
device control, shared IQ ring buffer (FStreamRing)
TSDRSpectrumAnalyser
GPU/OpenCL FFT → plots
TFMBroadcastReceiver (FReceiver)
2-thread chain → own TWaveOutPlayer
TAMBroadcastReceiver (FAMReceiver)
1-thread chain → own TWaveOutPlayer
IQ
(cursors)
ModeCombo: FM | AM
TSDRDevice subclass
capability-driven gain/freq + IQ correction
TSDRMain / TForm1
owns FRFSource, FAnalyser, FReceiver, FAMReceiver
Key relationship
• FReceiver and FAMReceiver are BOTH always created (FormCreate) and both point at the same FRFSource — but only one is
• ever Active. ModeComboChange sets both Active := False, then starts whichever the dropdown selects (StartSelectedReceiver).
• Each receiver owns its own TWaveOutPlayer instance — switching mode doesn't reuse a shared audio device handle, it opens
• a fresh one for whichever chain is now running.
• AM-only controls (BandwidthTrackBar, SynchronousCheckBox) are shown/hidden by ApplyListenModeVisibility based on ModeCombo.

## Slide 4
FM PIPELINE — SIGNAL PATH
Two-thread split: acquire (Stage A) → queue → demod (Stage B)
4
SDR_Radio — newVM Lazarus/FPC SDR receiver
1
TryReadEpoch
TSDRRFSource
IQ @ Fs_in
2
TComplexMixer
shift to baseband
LO=-(Tuned-Center)
3
TRationalResamplerC
decimate + AA filter
Fs_in → 200 kHz
STAGE A — TFMAcquireThread
FQueue
TBasebandQueue
cap=6, drop-oldest
4
TFMDemodulator
quadrature discrim.
±75 kHz dev.
5
TFMStereoDecoder
pilot-locked L−R
75µs de-emph.
6
TRationalResamplerS×2
L, R independently
200 kHz → 48 kHz
7
Volume + QueueStereo
AudioL/R * FVolume
→ TWaveOutPlayer
STAGE B — TFMDemodThread
Data type: complex baseband IQ (TVMobjC) through stage 3 → real multiplex/audio (TVMobjS) from stage 4 onward
Why split here, not elsewhere
• Live instrumented timing on real Raspberry Pi 5 + HackRF hardware showed the combined single-thread chain averaging
• a few percent OVER its per-epoch real-time budget, even after widening the epoch length and the wideband filter's
• transition band — TWaveOutPlayer's drift compensation was firing on nearly every epoch instead of occasionally,
• audible as a persistent low-level "motorboat" buzz plus occasional real underrun clicks.
• The chain naturally splits into two comparable-cost halves: Stage A (mixer + wideband resample, running at the high
• Fs_in rate) vs. Stage B (FM discriminator + 5-FIR-filter stereo decode + two resamplers, running at 200 kHz) — putting
• one on each thread lets them run truly concurrently on separate CPU cores instead of time-sharing one.
• FQueue hands Baseband epochs from A to B; a full queue drops the OLDEST entry rather than blocking Stage A — same
• "don't fall behind, skip forward" philosophy the shared IQ ring already uses.

## Slide 5
FM PIPELINE — STAGE DETAIL
Class, thread, rate, and role of each stage
5
SDR_Radio — newVM Lazarus/FPC SDR receiver
Stage
Class / call
Thread
Rate
Role
1
TryReadEpoch
Acquire (A)
— → Fs_in
Reads N samples for this consumer's own cursor from the shared IQ ring (thread-safe).
2
TComplexMixer.Process
Acquire (A)
Fs_in → Fs_in
Multiplies IQ by an NCO at −(Tuned−Center)Hz — shifts the chosen station to 0 Hz.
3
TRationalResamplerC.Process
Acquire (A)
Fs_in → 200 kHz
Rational resample; anti-alias filter (100 kHz cutoff) doubles as channel-selectivity filter. Result pushed onto FQueue.
4
TFMDemodulator.Process
Demod (B)
200 kHz
Quadrature discriminator, PeakDeviationHz=75000 → real FM multiplex (L+R, 19 kHz pilot, 23–53 kHz L−R).
5
TFMStereoDecoder.Process
Demod (B)
200 kHz
Pilot-locked L−R subcarrier decode + 75µs de-emphasis → independent L/R audio, still at 200 kHz.
6
TRationalResamplerS × 2
Demod (B)
200 kHz → 48 kHz
One instance per channel — same reusable resampler class as stage 3, real instead of complex.
7
QueueStereo
Demod (B)
48 kHz → card
Volume scale, then ALSA/waveOut write with drift compensation (see later slide).
• Epoch length is platform-dependent: 20ms / 60,000-sample cap on x86/Windows; widened to 32ms / 64,000 on ARM64
• (Raspberry Pi) to amortise fixed per-call TVMobjC/TVMobjS allocation overhead measured on real hardware.

## Slide 6
AM PIPELINE — SIGNAL PATH
Single-threaded chain: envelope or synchronous (PLL) detection
6
SDR_Radio — newVM Lazarus/FPC SDR receiver
1
TryReadEpoch
TSDRRFSource
IQ @ Fs_in
2
TComplexMixer
shift to baseband
LO=-(Tuned-Center)
3
TRationalResamplerC
decimate + AA filter
Fs_in → 2×BW
4
TAMDemodulator
envelope / PLL-sync
→ mono @ 2×BW
5
TRationalResamplerS
single (mono) channel
2×BW → 48 kHz
6
Volume + QueueStereo
duplicate mono → L=R
→ TWaveOutPlayer
TAMDSPThread — single thread, whole chain
BW = BandwidthHz (caller-selectable, default 5 kHz, range 1–10 kHz) — BasebandRateHz = BW×2 is the exact Nyquist rate for double-sideband AM
TAMDemodulator — two modes
• Envelope (Synchronous=False, default): |I+jQ| = sqrt(re²+im²) — the
• classic diode-detector equivalent. Simple, but selective fading
• distorts the recovered envelope directly.
• Synchronous (Synchronous=True): a 2nd-order Costas-loop-style PLL
• tracks the carrier phase (30 Hz loop bandwidth); rotating IQ by
• −phase gives a coherently-demodulated audio signal with better
• noise/fading rejection.
• Switchable LIVE with no chain rebuild — Process takes Synchronous
• as a per-call argument, so toggling doesn't reset PLL/DC state.
Why single-threaded, unlike FM
• FM's own two-thread split exists because TFMStereoDecoder alone
• runs FIVE FIR filters plus two further resamplers — measurably
• couldn't keep up on one core on real ARM64 hardware.
• TAMDemodulator is a plain O(N) loop with no filtering at all, and
• there's only ONE output resampler instead of two — an order of
• magnitude less per-sample work.
• Nothing has shown a need for a split here; revisit only if real-
• hardware timing ever shows a deficit, same evidence-driven approach
• that justified FM's own split (not done preemptively).

## Slide 7
AM PIPELINE — STAGE DETAIL
Class, rate, and role — plus live bandwidth changes
7
SDR_Radio — newVM Lazarus/FPC SDR receiver
Stage
Class / call
Rate
Role
1
TryReadEpoch
— → Fs_in
Reads N samples for this consumer's own cursor from the shared IQ ring.
2
TComplexMixer.Process
Fs_in → Fs_in
Shifts the chosen station to 0 Hz — identical to FM's own mixer stage.
3
TRationalResamplerC.Process
Fs_in → 2×BW
TransitionBW = Fs_in×2.5% (same fraction as FM's original, non-ARM64 value — AM's lighter downstream cost hasn't needed FM's extra headroom).
4
TAMDemodulator.Process
2×BW → 2×BW
Envelope sqrt(re²+im²) or PLL-coherent rotation, selected per-call by Synchronous. DC-average removed in envelope mode.
5
TRationalResamplerS.Process
2×BW → 48 kHz
TransitionBW = BasebandRateHz×20% — must scale with BW (2–20 kHz range), unlike FM's fixed 8 kHz.
6
QueueStereo(Audio, Audio)
48 kHz → card
Mono duplicated to both channels — AM broadcast carries no stereo subcarrier.
BandwidthHz — live-changeable, but not glitch-free
• Unlike TunedFrequencyHz (just an NCO frequency), BandwidthHz determines BasebandRateHz — every stage from the resampler
• onward must be rebuilt from scratch. SetBandwidthHz stops the DSP thread, tears down and rebuilds the chain, restarts it —
• a short audible discontinuity, the same kind of "click" a real radio's own bandwidth-filter switch makes.

## Slide 8
DATA COMMUNICATION
Shared IQ ring (3 consumers) + FM's internal handoff queue
8
SDR_Radio — newVM Lazarus/FPC SDR receiver
TSDRRingBuffer
device-level, single-consumer (inside TSDRDevice)
TSDRPollThread
sole caller of FDevice.TryReadEpoch
FStreamRing
array of TComplex8, ~1s capacity,
circular; guarded by FStreamLock
(TCriticalSection). 3 independent
read cursors, one per consumer below.
TSDRSpectrumAnalyser
GUI-thread timer, own cursor
TFMAcquireThread
FM Stage A, own cursor
TAMDSPThread
AM chain, own cursor
FQueue
cap=6
drop-oldest
TFMDemodThread
FM Stage B — pops FQueue, demod through QueueStereo
AM chain runs to
QueueStereo directly (no queue)
• FStreamRing's cursor model (owned by each caller, an opaque Int64) is unchanged from the original single-consumer fix —
• now serving three independent readers instead of two. A consumer that falls behind beyond ring capacity is skipped
• forward to the newest window rather than served stale data.
• FQueue is a SEPARATE, smaller handoff (Baseband epochs, not raw IQ) that exists only inside TFMBroadcastReceiver, guarded
• by its own TCriticalSection — unrelated to FStreamLock which protects FStreamRing.

## Slide 9
CONCURRENCY
FM (2 threads) vs. AM (1 thread) — full thread structure
9
SDR_Radio — newVM Lazarus/FPC SDR receiver
VENDOR
Vendor USB/IPC thread
libusb / rtlsdr_read_async / SDRplay API callback
ACQUIRE
TSDRPollThread
sole caller of FDevice.TryReadEpoch
FStreamRing
CONSUME
(cursors)
GUI TTimer
TSDRSpectrumAnalyser GPU FFT + repaint
TFMAcquireThread
FM Stage A: mixer + wideband resample → push FQueue
TAMDSPThread
AM whole chain → QueueStereo directly
FQueue
cap=6
TFMDemodThread
FM Stage B: demod + stereo + resample → QueueStereo
ALSA / waveOut (sync)
each receiver owns its own TWaveOutPlayer
GUI THREAD
• TForm1 message loop
• ModeCombo switches Active FM ↔ AM
• Freq/Volume/Bandwidth edits write fields directly, no lock
TSDRControlThread
coalesces RequestFrequencyHz; blocking vendor call off GUI thread; TThread.Queue back
Only one of the two lower paths is ever running at once (ModeCombo is mutually exclusive) — both drawn to show the full structure.

## Slide 10
CONCURRENCY DETAIL
Async retune — why frequency changes never freeze the UI
10
SDR_Radio — newVM Lazarus/FPC SDR receiver
1
User drags FreqEdit / ListenFreqEdit
GUI thread
2
RequestFrequencyHz(Hz) records latest value under FLock, returns immediately
GUI thread → TSDRControlThread
3
Execute loop picks up the LATEST pending Hz (coalescing, not queuing) and calls FDevice.SetFrequencyHz(Hz)
TSDRControlThread
4
TThread.Queue(nil, @...Applied) posts completion — never Synchronize (would block Execute on GUI responsiveness)
TSDRControlThread → GUI thread
5
OnFrequencyChanged fires; LastFrequencyChangeOk / LastError read by the form
GUI thread
The problem this solves
• Each backend's SetFrequencyHz makes a synchronous, potentially slow call into the vendor driver/API while streaming
• (e.g. SDRplay's sdrplay_api_Update is a real IPC round-trip to sdrplay_apiService.exe, not a fire-and-forget register write).
• Calling it directly from the GUI thread — as the original FreqEdit/keypad handlers did — froze the whole message loop
• for however long that call took, under real concurrent load (TSDRPollThread + a running receiver chain + the spectrum
• analyser's GPU work all competing for the same USB/IPC bandwidth) — long enough that Windows would mark the window
• ‘Not Responding’ and a user would reasonably kill it via Task Manager.
• Shared by both receivers today: whichever of FReceiver/FAMReceiver is Active reads the same FRFSource.TunedFrequencyHz-
• style mixer update, unaffected by this control-thread mechanism (only the RF front end's own retune goes through it).

## Slide 11
AUDIO OUTPUT
TWaveOutPlayer — per-receiver instances + ALSA drift fix
11
SDR_Radio — newVM Lazarus/FPC SDR receiver
Windows — waveOut
Ring of 16 WAVEHDR buffers (~320ms headroom). QueueStereo submits via waveOutWrite; a full ring DROPS the epoch rather than blocking.
Linux — ALSA (libasound.so.2, dlopen'd)
snd_pcm_open(NONBLOCK) + snd_pcm_set_params (~1s requested latency). EAGAIN → drop epoch, EPIPE/underrun → snd_pcm_recover.
EACH RECEIVER OWNS ITS OWN INSTANCE
TFMBroadcastReceiver.FPlayer and TAMBroadcastReceiver.FPlayer are separate objects — switching ModeCombo opens/closes independently.
FIXED 2026-08-22
Root cause of intermittent audio: unbounded ALSA ring-buffer drift
• Prior fixes (widen buffer, fix short-write handling) only pushed the symptom out: nothing paced QueueStereo calls to the sound card's actual playback clock, so any persistent mismatch (SDR clock vs. sound-card clock, OS scheduling jitter, GPU/spectrum contention) drained or filled the ring without bound.
• Confirmed with a synthetic-tone test harness (no SDR hardware at all) that still accumulated underruns at a rock-steady 20ms epoch cadence — proving it wasn't a hardware-timing artifact.
• Fix: the ALSA backend reads queued-frame count via snd_pcm_delay and applies a proportional correction each epoch (duplicate/drop a few frames, clamped to 128, gain 0.1, dead-banded), paired with widening requested latency to ~1s.
• The subsequent FM two-thread split (earlier slides) addressed a SEPARATE, related symptom on ARM64: the single-thread chain running slower than real time, making this same drift-compensation fire on nearly every epoch — fixing the compute deficit, not the compensation mechanism itself.